## Slide 1
GridWise AI
Grid Load Optimisation & Renewable Energy Performance Advisor
IBM Bob AI Hackathon | Track: AI | Team: Outliers
WARNING: All data is SYNTHETIC / DEMO — not real telemetry
Notes: Title slide. GridWise AI is a full-stack grid intelligence platform integrating XGBoost load forecasting, physics-based renewable models, anomaly detection, root cause analysis, grid optimisation, and IBM Bob conversational interface.

## Slide 2
The Problem
Grid operators face 5 simultaneous challenges:
1. DEMAND SPIKES — When will load exceed capacity?
2. RENEWABLE MONITORING — Which assets are underperforming?
3. ROOT CAUSE AMBIGUITY — Weather fault? Equipment fault? Data error?
4. SUPPLY-DEMAND OPTIMISATION — BESS? DR? Backup generation?
5. CURTAILMENT — How much renewable energy is being wasted?
No existing tool integrates all five with a conversational AI interface.
Operators switch between disconnected systems while the grid changes.
Notes: The problem is multi-dimensional: demand forecasting, renewable monitoring, fault diagnosis, optimisation, and curtailment minimisation. Each exists in isolation today.

## Slide 3
Our Solution — GridWise AI
XGBoost Load Forecast --> Physics Renewable Models --> Anomaly Detection
|
v
Root Cause Analysis --> Grid Optimisation Engine --> Curtailment Minimiser
|
v
Operator Brief Generator --> FastAPI Backend
| |
v v
IBM Bob (MCP Server) Operator Dashboard
Stack: Python / FastAPI / XGBoost / pandas / Node.js / IBM Bob MCP / HTML+JS
Notes: Full-stack chain from raw data to IBM Bob conversational interface. All steps are deterministic and explainable.

## Slide 4
IBM Bob Integration — 9 MCP Tools
get_grid_status -> Load, capacity, reserve margin, risk level [RULE-BASED]
get_load_forecast -> 24h XGBoost demand forecast [ML MODEL]
get_spike_risks -> Per-hour LOW/MEDIUM/HIGH/CRITICAL risk [RULE-BASED]
get_renewable_forecast -> Expected solar + wind generation [PHYSICS MODEL]
get_asset_anomalies -> Underperforming assets, performance ratios [RULE-BASED]
diagnose_asset -> RCA: weather vs unexplained loss [HEURISTIC RCA]
get_optimisation_plan -> BESS / DR / backup dispatch plan [DETERMINISTIC]
get_curtailment_plan -> Curtailment minimisation breakdown [ARITHMETIC]
generate_operator_brief-> Full 14-section operator brief [AGGREGATED]
KEY PRINCIPLE: Bob reads computed backend results. It never fabricates measurements.
Notes: Bob calls 9 MCP tools that each hit a specific FastAPI endpoint. Every number Bob cites has a traceable origin in the computation chain.

## Slide 5
Demo Scenario D — Spike + Inverter Fault
Scenario: August 14, 2023 — Hot summer day
SPIKE: Evening demand rising to 2,115 MW (reserve margin ~12%)
FAULT: SOL-02 (Sunfield Beta) at 18% capacity factor
-- Clear sky, 950 W/m2 irradiance
-- No weather excuse: unexplained loss = 49.8 MW
-- Diagnosis: inverter / string issue [52% confidence]
-- Inspection RECOMMENDED
OPTIMISATION:
BESS discharges 178 MWh to cover evening deficit
Demand response activated for 7 intervals
Backup generation required for 4 peak intervals
CURTAILMENT:
9.2 MWh potential midday surplus fully absorbed by BESS
Notes: This is the combined hackathon demo scenario. Run GET /demo to reproduce all results deterministically.

## Slide 6
Evidence-Based RCA — Our Strongest Feature
The RCA engine (root_cause_analysis.py) is the core innovation:
1. Total loss = expected - actual generation
2. Weather-explained loss calculated from:
- Cloud cover transmissivity model
- Irradiance reduction factor
- Temperature derating coefficient
- Wind speed vs power curve
3. Unexplained loss = total - weather explained
4. Confidence-scored cause candidates returned
5. Inspection triggered only when unexplained > threshold
Example (SOL-02, clear sky day):
Expected: 63.0 MW | Actual: 11.5 MW | Total loss: 51.5 MW
Weather explained: 1.7 MW (high temperature only)
Unexplained: 49.8 MW --> INSPECTION REQUIRED
Top cause: inverter_or_string_issue [52% confidence]
This is NOT a black box. Every step is traceable arithmetic.
Notes: The RCA correctly distinguishes weather-caused losses from genuine equipment faults. This is the key differentiator from simpler threshold alarms.

## Slide 7
Test Results & Validation
62 pytest tests | 0 failed | 0 warnings
Phase 1 Tests (38):
Load forecasting: features, leakage prevention, chronological split
Anomaly detection: normal/warning/critical, nighttime suppression
Root cause analysis: weather vs unexplained, weather-explained = no fault
Spike detection: risk classification, reserve margin formula
Renewable models: solar physics, wind power curve
Phase 2 Tests (24):
Grid optimisation: deficit, surplus, empty BESS, full BESS, power limits
Energy conservation: supply >= demand after dispatch
Curtailment accounting: avoided + unavoidable = potential
Scenarios A/B/C: normal, spike, surplus+fault
Multiple anomalous assets, weather vs unexplained RCA
Model Metrics (XGBoost, synthetic data):
Train R2=0.996 MAE=19 MW
Val R2=0.986 MAE=24 MW
Test R2=0.900 MAE=49 MW
Notes: All 62 tests pass. The XGBoost model achieves R2=0.90 on held-out synthetic test data with a strictly chronological split.

## Slide 8
Thank You
Team Outliers | IBM Bob AI Hackathon | Track: AI
Run the demo:
uvicorn src.backend.main:app --port 8000 --reload
http://localhost:8000/dashboard
GitHub: bob-ai-hackathon-outliers | API Docs: /docs | Demo: /demo
Notes: Thank you. Questions welcome. Run GET /demo for the full combined scenario pipeline result.